## Slide 1: Tecnologias Digitais para Sistemas de Rádio Definidos por Software
Nuno Borges Carvalho
José Neto Vieira
Digital Technologies for Software Defined Radio Systems
Radio Transceivers

## Slide 2
Analog Radio
  Conversion made by hardware
  Filtering and demodulation done with electronic components
Software Defined Radio

## Slide 3
Software Defined Radio
  Radio in which the processing is completelly digital.
J. Mitola, “The software radio architecture,” IEEE Communications Magazine, vol. 33, nº 5, pp. 26–38, May 1995
Joe Mitola says, "A software radio is a radio whose channel modulation waveforms are defined in software. That is, waveforms are generated as sampled digital signals, converted from digital to analog via a wideband DAC and then possibly upconverted from IF to RF. The receiver, similarly, employs a wideband Analog to Digital Converter (ADC) that captures all of the channels of the software radio node. The receiver then extracts, downconverts and demodulates the channel waveform using software on a general purpose processor."
Software Defined Radio

## Slide 4
A Software Defined Radio (SDR) system is a radio communication system where components that have typically been implemented in hardware (i.e. mixers, filters, amplifiers, modulators/demodulators, detectors. etc.) are implemented using software on a personal computer.
Definition by SDR Forum-
Software defined radio is used to describe radios that provide software control of a variety of modulation techniques, wide-band or narrow-band operation, communications security functions (such as hopping), and waveform requirements of current and evolving standards over a broad frequency range.
Software Defined Radio

## Slide 5
Actual SDR systems ….
Some parts in the analog domain, some parts in the digital domain.
Software Defined Radio

## Slide 6
SDR has been conquering the analog world, moving from base band to RF.
Variable Frequency Oscillator
Local Oscillator
Antenna
Bandpass Filter
RF
IF
Baseband
ADC/DAC DSP
Software Defined Radio

## Slide 7
Variable Frequency Oscillator
Antenna
RF
IF
Baseband
ADC/DAC DSP
All Digital
SDR has been conquering the analog world, moving from base band to RF.
Software Defined Radio

## Slide 8
Antenna
RF
IF
Baseband
ADC/DAC DSP
All Digital
All Digital
SDR has been conquering the analog world, moving from base band to RF.
Software Defined Radio

## Slide 9
.
In a real SDR, multi-band and multi-standard we should be aware of:
  Adaptive filtering in order to reduce noise and subsequently increase of SNR.
  Guarantee the out-of-band rejection for all standards and change in bandwidth.
Software Defined Radio

## Slide 10
Sensitivity is the minimum power a receiver can have at the input in order to guarantee a minimum SNR.
NF is called the noise figure, k is the Boltzmann constant, T the room temperature and B the bandwidth.
Software Defined Radio

## Slide 11
Dynamic range is nothing more that the difference between the minimum and the maximum power the transceiver (receiver) can dealt with.
Where Pmax is normally calculated as the maximum power that will saturate the receiver front end, so that the auto-generated nonlinear distortion is similar to the seek SNR.
Software Defined Radio

## Slide 12
.
Problems associated with large signal variations, mainly dynamic range limitations.
Software Defined Radio

## Slide 13
.
At the transmitter PAPR can degrade
  Digital to Analog Converters – DAC
  Power Amplifiers
At Receiver
  Analog to Digital Converter
Software Defined Radio

## Slide 14
.
In the transmitter.
Software Defined Radio

## Slide 15
Analog Data.
Digital Data.
Software Defined Radio

## Slide 16
Sampling
Output is a replica of the input at certain instants of time.
Software Defined Radio

## Slide 17
Quantization
Actually transform the input signal amplitude into several quantizer levels Q=2N-1
Quantization error:
Quantization interval:
Software Defined Radio

## Slide 18
  Flash ADC
  Delta-tracking, uses DAC’s
  Ramp-compare ADC;
  Sigma-Delta .
  Pipeline
Several configurations can be used for ADC’s:
Software Defined Radio

## Slide 19
.
Ideal transmitter in SDR:
  PWM modulator, digital signals goes till the antenna:
Software Defined Radio

## Slide 20
.
By cognitive we can understand:
Original definition by Joseph Mitolla (1999)
A radio that employs model based reasoning to achieve a specified level of competence in radio-related domains
Simon Haykin’s Definition:
An ambient-aware, intelligent radio which learn from its surroundings and adapt itself to:
  Highly reliable communication, anywhere, anytime;
  Efficient use of Radio Spectrum;
Cognitive Radio

## Slide 21
.
CR – Cognitive Radio PBAR – Policy-Based Adaptive Radio
RFI – Request for Information SCR – Software Controlled Radio
SDR – Software Defined Radio SR – Software Radio
Note: SDR currently is practical for some applications such as commercial wireless basestations, but not for some wireless handsets. Cost, power, size and weight are critical design requirements that must be considered when considering the use of advanced radio technologies.
Increasing Flexibility and Reconfigurability
SCR
SCR + SDR baseband (for some applications)
Ideal Software Radio
SCR + SDR baseband + SDR RF
Hardware Radio
1995
2005
2025
2015
2004: First SDR device approved by FCC
1995: First RFI on SDR
SR
SDR
Increasing use of software in advanced radios
CR
PBAR
Hardware radio includes firmware and therefore may have significant operational flexibility.
IEEE 1900 Committee

## Slide 22
.
Develop Request
RF Resource Request
Process Request
Determine Opportunities
Select Opportunities
RF Transmit Plan
Bound: Yes/No
Unbound: Binding
Constraints
Cognitive Radio

## Slide 23
Non Cognitive Radios:
Cognitive Radios:
Cognitive Radio

## Slide 24
In a cognitive radio we should be able to:
Create our own waveforms,
Negotiate different interfaces
Maintain QoS be managing is radio
Practically it should be:
SDR +
Have some kind of intelligence
Environment aware
Be capable of sensing the environment
Cognitive Radio

## Slide 25
Urgent
Allocate Resources
Initiate Processes
Negotiate Protocols
Orient
Infer from Context
Select Alternate
Goals
Plan
Normal
Immediate
Learn
New
States
Observe
Outside
World
Decide
Act
User Driven
(Buttons)
Autonomous
Infer from Radio Model
States
Generate “Best”
Waveform
Establish Priority
Parse Stimuli
Pre-process
Cognition cycle
[Mitola_99]
Cognitive Radio

## Slide 26
Cognitive Radio

## Slide 27
D/A
PA
LNA
A/D
IFFT
FFT
ADAPTIVE
LOADING
INTERFERENCE
MEAS/CANCEL
MAE/
POWER CTRL
CHANNEL
SEL/EST
TIME, FREQ,
SPACE SEL
LEARN
ENVIRONMENT
QoS vs.
RATE
FEEDBACK
TO CRs
Sensing Radio
Wideband antenna, PA and LNA
ADC and DAC should have high sampling rates and moderate resolution
Simultaneous Tx and Rx
Allows MIMO
Physical Layer
OFDM Transmission
Spectrum monitoring
Frequency selection, modulation and dynamic power control
Non ideal equalization of the analog parts
MAC Layer
Optimize the transmission parameters
Adaptive change of the transmission rates
Negotiate resources
RF/Analog Front-end
Digital Baseband
MAC Layer
Cognitive Radio