## Slide 1: Software Defined Radio PhD Program on Electrical Engineering
Sampling Theory and Quantization
José Vieira

## Slide 2: Sumary
The USRP kits in the Lab
Sampling of low-pass signals
Sampling of band-pass signals
Second order sampling
Quantization

## Slide 3: USRP 1

## Slide 4: USRP
Four 12bit 64Ms/s ADCs
Four 14bit 128Ms/s DACs
USB 2.0 with 32MB/s

## Slide 5: USRP – FPGA pre-programmed front-end
The FPGA has a digital down converter
The frequency of the Numerical Controlled Oscillator and the decimation factor can be changed
The output is transmitted via USB to the PC
The remaining processing is performed on the PC.

## Slide 6: USRP – Architecture general overview

## Slide 7: USRP 2

## Slide 8: USRP 2
Use with GNU Radio, LabVIEWTM and SimulinkTM
Modular Architecture: DC-6 GHz
Dual 100 MS/s, 14-bit ADC
Dual 400 MS/s, 16-bit DAC
DDC/DUC with 25 mHz Resolution
Up to 50 MS/s Gigabit Ethernet Streaming
Fully-Coherent MIMO Capability
Gigabit Ethernet Interface to Host
Spartan 3A-DSP 3400 FPGA (N210)

## Slide 9: USRP 2

## Slide 10: Sampling of low-pass signals
The Sampling Theorem
We can describe the sampling process as a multiplying the signal x(t) by a pulse train of Dirac pulses
Consider a low-pass signal x(t) with bandwidth B. Then, if we sample this signal at a rate greater than 2B is possible to reconstruct the original signal from the samples.

## Slide 11: Sampling of low-pass signals
In the Fourier transform domain
Fourier transform of the signal p(t)
Notes: Colocar aqui uma figura com o pente no tempo e na freq

## Slide 12: Aliasing
When the sampling frequency is not enough, aliasing occurs due to the overlap of the spectrum components

## Slide 13: Sampling a Low-pass Signal
Low pass filter

## Slide 14: Uniform sampling of band-pass signals
Consider a band-pass signal x(t) with carrier frequency fc and bandwidth B.
The maximum frequency of this signal is
Using the Nyquist sampling theorem for low-pass signals the sampling frequency fs for the signal x(t) should be

## Slide 15: Uniform sampling of band-pass signals
For modulated signals x(t) where the frequency of the carrier fc is much larger than the signal bandwidth, this form of sampling is impracticable.
However, there is a version of the Nyquist theorem for band-pass signals
If a signal as bandwidth B, then the sampling frequency fs should be greater than 2B in order to be possible to recover the original signal from the samples.

## Slide 16: Sub-Sampling Using a Band-pass Filter
Fs=2B
2B
2B

## Slide 17: Sub-Sampling
The sampling frequency fs should be properly chosen in order to match the carrier frequency, we could have fc=kfs, with k an integer.
In certain systems we can use oversampling and perform the band-pass filtering in the digital domain.
As the resultant signal is oversampled it can decimated. Using polyphase decomposition of the anti-aliasing filters an efficient implementation is possible.

## Slide 18: Sampling of band-pass signals
The Nyquist zones

## Slide 19: Second Order Sampling
The second order sampling is a form of sub-sampling with down conversion that gives the in-phase and quadrature components directly.

## Slide 20: Second Order Sampling

## Slide 21: Oversampling and Digital Decimation
Fs>2B
2B
>2B

## Slide 22: Quantization

## Slide 23: Fixed Point Multiplication with the Q15 Format

## Slide 24: Integer Multiplication

## Slide 25: Example
0.6796875*0.9296875 =0.63189697265625
119 *87 =10353
0.1110111 *0.1010111 =00.10100001110001
=0.625

## Slide 26: Fixed Point Arithmetic
Avoiding the Overflow
  Scaling
  Saturated arithmetic
Truncation
Rounding
  Rounding to the nearest
  Convergent rounding

## Slide 27: Scaling
Consider a system with a frequency response having a absolute value maximum given by
To avoid the saturation of the signal numerical representation at the output of the system (overflow), we have to scale the input signal by multiplying with the scaling factor 1/A.

## Slide 28: Scaling

## Slide 29: Scaling on the inner points
Consider a second order IIR notch filter.
Also consider that the maximum absolute value of the frequency response is 0dB.
What would be the maximum absolute value of the frequency response of

## Slide 30: Pole-zero Map

## Slide 31: Frequency Response

## Slide 32: Scaling in the Inner Points
To avoid the overflow on the inner point of the IIR filter we have to reduce the amplitude of the input signal by the maximum absolute value of the transfer function between the input and the inner point.
Then, in order to replace the unitary in/out gain on the pass-band we have to set an inverse gain on the output
Result: Signal to Noise ratio degradation

## Slide 33: Quantization

## Slide 34: Quantization
|x|≤1
q = nº of quantization steps
  2/q , quantization step
b = nº of quantization bits
q = 2b

## Slide 35: Quantization
|x|≤1
q = nº of quantization steps
  2/q , quantization step
b = nº of quantization bits
q = 2b

## Slide 36: Quantization Noise

## Slide 37: Signal to Quantization Noise Ratio
The signal to quantization noise ratio is a function of the number of bits.
Each extra bit reduces the signal to noise ratio by 6dBs
With 16 bits we get around 100dB of signal to noise ratio

## Slide 38: Scaling and Quantization Noise
If in a 16 bit system the scaling factor is set to A=256, then the signal to noise ratio will be 52dB instead of 100dB
Note that if we have used a floating point arithmetic the scaling of the inner point was not necessery. The signal to noise ratio would be 100dB.

## Slide 39: Rounding Error on FIR Filters
16bits Accumulator

## Slide 40: Rounding Error in FIR Filters
32bits Accumulator
The quantization noise does
not increase with the
number of coeficients

## Slide 41: Rounding Error on IIR Filters
For the IIR filters, due to the feedback, an accumulator with extra bits does not solve the quantization error problem.
Stability issues when the poles are near the unitary circle. Due to the quantization problems the poles could be moved to out of the unitary circle.
Limit cycles, which are small output periodic signals when no input is applied.

## Slide 42: Effects of the Filter Coefficients Quantization
FIR filters
  The frequency response of the filter with the quantized coefficients can be quite different of the designed one
  This can be a difficult problem to solve for filters with a large number of coefficients.
IIR filters
  Stability problems due to the placement of the poles near the unit circle
  The frequency response of the quantized version can be quite different due to the high precision needed for the pole-zero placement

## Slide 43: Non-uniform Quantization
If the Probability Density Function (pdf) of the input signal is known we can take advantage of this knowledge using non-uniform quantization.
The uniform quantizer is optimal only for signals with a constant pdf.
Example: The voice signal has a Laplacian pdf. The small amplitudes are more probable than the larger ones.
Notes: Ser mais rigoroso na apresentação da quantização não uniforme ideal

## Slide 44: Signal with a Laplacian PDF

## Slide 45: Dithering
When the amplitude of the signal is too small when compared with the minimum quantization step, is possible to obtain a digital representation of this signal by using dithering
Dithering example with 5 levels of quantization {-1,0.5,0,0.5, 1} and thresholds on {-0.5,-0.25,0.25,0.5}
Notes: Melhorar a descrição do dithering e introduzir referências

## Slide 46: Dithering
A dithering signal with an uniform distribution with a maximum amplitude equal to half the quantization step has the effect of flatting the quantization noise spectrum.

## Slide 47: Bibliography
John G. Proakis and Dimitris G. Manolakis, “Digital Signal Processing, Prentice Hall, 2007. (Chapter 9)
Jeffrey H. Reed, “Software Radio”, Prentice Hall, 2002. (Chapter 5)