## Slide 1: Software Defined Radio PhD Program on Electrical Engineering
Multirate Systems and CIC Filters
José Vieira

## Slide 2: Summary
Interpolation
Decimation
Time and Frequency Multiplexing
Changing the Sampling Rate by a Rational Factor
The Noble Identities
The Polyphase Decomposition
Filter banks
  The two channels case
  Alias cancelation
  Perfect reconstruction
Tree filter banks
Time frequency decomposition

## Slide 3: Bibliography
Sebenta de Processamento Digital de Sinal do Prof. Tomás Oliveira e Silva
P. P. Vaidyanathan, “Multirate Systems and Filter Banks”, Prentice Hall, 1993.
Recommended reading from this book
  Chapter 4
  Sections 5.0, 5.1, 5.2, 5.3, 5.3.1, 5.3.6, 5.4, 5.5, 5.8, 5.9
Optional reading
  Sections 5.6 and 5.7

## Slide 4: Filter Banks
The analysis filter bank splits the input signal into several frequency bands
The synthesis filter bank combines the bands into one signal
The coding or other processing is performed on each band

## Slide 5: The Two Channel Case
The input signal is split into two frequency components, low and high.
The analysis has a low pass-filter H0(z) and a high-pass filter H1(z). That way F0(z) is also low-pass and F1(z) high-pass.
The signals x0 and x1 only have half the bandwidth of the input signal x.

## Slide 6: Designing the Filters
Ideal Filters
Non-overlapping Filters
Overlapping Filters

## Slide 7: Decimated Two-Channel Filter Bank
The sampling rate of the signals x0 and x1 are reduced by a factor of two
The bandwidth of the signals x0 and x1 is also reduced by a factor of two.
Due to this, it is not possible to avoid aliasing on the the signals x0 and x1
Notes: Fazer aqui uma simulação manual do sistema para h0={1,1} e x={1,1}

## Slide 8: Aliasing in a Two-Channel Filter Bank
Aliasing component after the decimators
Spectrum before the decimators

## Slide 9: Canceling the Aliasing
The Z transform of the output signal can be written as a function of X(z) and X(-z)
To cancel the aliasing component we should have
This can be obtained by doing

## Slide 10: The Transfer Function and Perfect Reconstruction
When the alias is canceled, the filter bank has a transfer function given by
If this transfer function can be put in the form
Then we say that the filter bank has
Perfect Reconstruction

## Slide 11: Polyphase Decomposition of a Filter Bank – Two channel case
If the filters of the two channel filter bank are represented using the polyphase decomposition we can move the decimators and expanders and get the following system
And the perfect reconstruction is obtained when

## Slide 12: Polyphase Decomposition of a Filter Bank – The General Case

## Slide 13: Tree Filter Banks
The time frequency decomposition

## Slide 14: Cascaded Integrator-Comb (CIC) Filters
The CIC filters are an efficient implementation of “Moving Average Filters”.
A “Moving Average Filter” has the following impulse response
and the Z transform
the transfer function would be given by

## Slide 15: Moving Average Filter

## Slide 16: Moving Average Filter – CIC Version Cascaded Integrator-Comb Filters
Only two additions per output sample regardless the value of D

## Slide 17: CIC Filters for Decimation

## Slide 18: CIC Filters for Decimation – Efficient Version

## Slide 19: Aliasing in Decimation with CIC Filters

## Slide 20: Mth Order CIC FIlters

## Slide 21: Direct Digital Synthesis – DDS

## Slide 22: Direct Digital Synthesis – DDS
ROM LUT - ROM Look Up Table

## Slide 23: Direct Digital Synthesis
Advantages over the analog generation of signals
  Precision on the generated frequency
  Flexibility. The parameters of the generated signal can be easily changed
  Controlled phase on frequency changing
  Smaller size
  Generation of high quality signals with small distortion

## Slide 24: Periodic Arbitrary Waveform
It is possible to generate any waveform by storing one period on the ROM LUT
If the period is too long we need a large memory
However, sinusoid generation is the most common case

## Slide 25: Sinusoid Generation by DDS
It is possible to generate a sinusoid using DDS with a phase accumulator
Consider a continuous sine wave
The sine function is periodic because
If we consider the discrete case we will have

## Slide 26: Sinusoid Generation by DDS
To have a periodic sine wave the value at the sample n must be equal to the value at the sample n+N.
This implies that
where k is an integer. Rearranging this equation we have
As N and k are integers fs/f0 must be a rational number in order the discrete sine to be periodic

## Slide 27: Sine Generation with DDS
The LUT should have a complete sine period

## Slide 28: Sine Generation with a Phase Accumulator
Returning to the expression of the sampled sinusoid
The phase increment finc is also known as the normalized frequency

## Slide 29: Sine Generation with a Phase Accumulator

## Slide 30: Sine Generation with a Phase Accumulator
Sample points on the unit circle
in radians
Each point on the unit circle represents a sample of the sin function to store on the table
The minimum phase increment is 2p/N
This is also the frequency resolution of the generator

## Slide 31: Sine Generation with a Phase Accumulator
Sample points on the unit circle
in Hertz
If we normalize to Hertz we can read directly the generated frequency
The resolution is fs/N

## Slide 32: Sine Generation with a Phase Accumulator
Sample points on the unit circle
normalized to N
Instead of dealing with arithmetic mod 2p we can normalize to N and work with the more convenient arithmetic mod N
The minimum frequency is achieved with a step of 1

## Slide 33: Sine Generation with a Phase Accumulator
Sample points on the unit circle
normalized to N
Sin table with N samples

## Slide 34: Frequency Resolution and LUT Size
If the phase increment is represented by an integer then the minimum value is 1
As the LUT has a whole sine period, if it has N samples the maximum value for the generated sine period is
Then the minimum frequency is
This f0 corresponds to a phase increment of 1 and it is the frequency resolution of the generator

## Slide 35: Frequency Resolution and LUT Size
To guarantee the frequency resolution we should have
If we have fs=100MHz and f0=10Hz then N must be larger than 1e7. We will need a counter with 24 bits and a table with 16MB.
This table size is not reasonable. Fortunately, several techniques can be used to reduce the table size.

## Slide 36: Techniques to Reduce the LUT Size
Use a fractional counter where only the integer part is used to address the LUT
Store only one quadrant of the sine period
Interpolation using Taylor’s Series Expansion
Interpolation using trigonometric identities

## Slide 37: Reducing the LUT Size

## Slide 38: Spurious Frequencies
The main frequency of a DDS is given by
When we have the relation
Example 1: N=16 and Dr=2
Example 2: N=16 and Dr=6
We have a secondary period with 8 samples

## Slide 39: Spurious Frequencies
Example 1

## Slide 40: Spurious Frequencies
Example 2

## Slide 41: Interpolation Using Trigonometric Identity
To increase the resolution of the sine function without increasing the size of the LUT we can use the following trigonometric identity
The angle α is a coarse table having the sine values for angles around the circle.
The angle β as a fine resolution from zero to the first value of α.

## Slide 42: Interpolation Using Trigonometric Identity
Coarse angle α
Fine angle β

## Slide 43: Interpolation Using Trigonometric Identity
So we can use two tables, one for α and another one for β.
However, if αmin is small enough, then the angle β is always close to zero, and we can simplify the previous equation

## Slide 44: Interpolation Using Trigonometric Identity
With this technique is possible to evaluate the sine function with a great resolution using a small LUT and a few more calculations and two LUT reads.
Example for a LUT with 80 samples
Notes: Adicionar as condições do gráfico

## Slide 45: Main Source of Errors on DDS Systems
Amplitude truncation – lack of bits on the LUT
Phase truncation – lack of bits to address the LUT
DAC resolution – the number of bits of the DAC